Controller Area Network
CAN CC / CAN FD / CAN XL

---
CAN data packets on the bus - simplified for nerds
Media access by CSMA/CR (resolution) sometimes CSMA/CA (avoidance)
Structure of a CAN CC (aka Classical CAN, CAN 2.0B) frame:
Simplified: [CAN Identifier] [Data length] [Data 0..8]
Content addressing (by CAN Identifier & CAN Bus)
No MAC number / Node addresses / ARP / Routing – just plain OSI Layer 2
CAN CC-only controller breaking upgrade to CAN FD (ISO 11898-1:2015)
S
O
F
CAN-ID
(11/29 Bit)
DLC
(4 Bit)
DATA
(0-8 Byte)
Checksum
(15 Bit)
D
E
L
EOF
(7 Bit)
R
T
R
I
D
E
r
e
s
A
C
K
D
E
L
Arbitration
Control
Data
Check
Acknowledge

---
Safe but not secure
Serial communication protocol, ISO Standard 11898
Two wires: Unshielded twisted pair, terminated
Transfer rate up to 1MBit/s (CAN CC) and up to ~4MBit/s (CAN FD)
Invented by Robert Bosch GmbH, 1983
Only defines the Media Access Layer
CAN
ECU
CAN
ECU
CAN
ECU

---
Multi-master bus topology
Unlike point-to-point Ethernet all nodes use the same wire
CAN
ECU
CAN
ECU
CAN
ECU
The wires are named CAN_Low and CAN_High

---
Differential potentials for electro magnetic interference (EMI)
A glitch occurs on both lines at the same time ➔ difference remains stable
CAN
ECU
CAN
ECU
CAN
ECU
Unshielded twisted pair

---
Bus termination to prevent reflection/echos
Terminate data transmission to prevent reflection/echos a the end of the wire
CAN
ECU
CAN
ECU
CAN
ECU
120 Ohms each ➔ 60 Ohms total

---
Data acknowledge by receive node
Only acknowledged CAN frames are valid CAN frames.
CAN
ECU
CAN
ECU
CAN
ECU
Protocol violations lead to a destroyed CAN frame (error flag)

---
Switching from CAN CC to CAN FD by using the reserved bit
0 0 0
S
O
F
CAN-ID
(11 Bit)
R
T
R
I
D
E
r
0
DLC
(4 Bit)
DATA
(0-8 Byte)
Checksum
(15 Bit)
D
E
L
A
C
K
D
E
L
EOF
(7 Bit)
Arbitration
Control
Data
Check
Acknowledge
Arbitration Bitrate
FD Data Bitrate (BRS = 1)
Arbitration Bitrate
S
O
F
CAN-ID
(11 Bit)
r
1
I
D
E
Arbitration
r
0
F
D
F
0 0 1 0
DLC
(4 Bit)
DATA
(0-64 Byte)
Checksum
(17/21 Bit)
StuffCNT (4 Bit)
D
E
L
EOF
(7 Bit)
A
C
K
D
E
L
Control
Data
Check
Acknowledge
B
R
S
E
S
I
Breaking reserved bits: new funtionality & incompatibility

---
CAN FD – new bits and definitions in detail
0 0 1 0
S
O
F
CAN-ID
(11 Bit)
r
1
I
D
E
F
D
F
r
0
B
R
S
E
S
I
DLC
(4 Bit)
DATA
(0-64 Byte)
Checksum
(17/21 Bit)
StuffCNT (4 Bit)
D
E
L
A
C
K
D
E
L
EOF
(7 Bit)
Arbitration
Control
Data
Check
Acknowledge
no RTR function
Error State Indicator
Bit Rate Switch
Flexible Data Frame
DLC
0
1
..
7
8
9
A
B
C
D
E
F
DATA LEN
0
1
..
7
8
12
16
20
24
32
48
64
non-linear(!!) mapping : DLC ➔ payload length

---
Compatible data structure layout for CAN CC and CAN FD
CAN CC data structure (the len element was formerly named can_dlc)
CAN FD data structure
struct can_frame {
        canid_t can_id; /* 32 bit CAN_ID + EFF/RTR/ERR flags */
        __u8 len; /* frame payload length in byte (0 .. 8) */
        __u8 __pad; /* padding */
        __u8 __res0; /* reserved / padding */
        __u8 len8_dlc; /* optional DLC for 8 byte payload length */
        __u8 data[8] __attribute__((aligned(8)));
};
struct canfd_frame {
        canid_t can_id; /* 32 bit CAN_ID + EFF/RTR/ERR flags */
        __u8 len; /* frame payload length in byte (0 .. 64) */
        __u8 flags; /* additional flags for CAN FD */
        __u8 __res0; /* reserved / padding */
        __u8 __res1; /* reserved / padding */
        __u8 data[64] __attribute__((aligned(8)));
};

---
CAN FD data structure – dual use with CAN CC layout
Writing CAN CC data into a CAN FD data structure creates valid content.
CAN ID
LEN
0
1
2
3
4
5
6
7
CAN ID
LEN
FD
RES
RES
--------------
0
1
2
3
4
5
6
7
60
61
62
63
struct canfd_frame
struct can_frame
#define CANFD_BRS 0x01 /* bit rate switch (second bitrate for payload data) */
#define CANFD_ESI 0x02 /* error state indicator of the transmitting node */
#define CANFD_FDF 0x04 /* mark CAN FD for dual use of struct canfd_frame */
PAD
RES
8dlc
Writing direction into data structure

---
How to activate CAN FD on a CAN_RAW socket
Reading and writing CAN data structures with CAN CC
Switch the socket into CAN FD mode with setsockopt() syscall
struct can_frame cframe;
int s = socket(PF_CAN, SOCK_DGRAM, CAN_RAW);
(..)
nbytes = read(s, &cframe, sizeof(struct can_frame));
struct canfd_frame cframe;
int s = socket(PF_CAN, SOCK_DGRAM, CAN_RAW);
setsockopt(s, SOL_CAN_RAW, CAN_RAW_FD_FRAMES, ...);
(..)
nbytes = read(s, &cframe, sizeof(struct canfd_frame));

---
Switching from CAN CC to CAN FD by using the reserved bit (recap)
0 0 0
S
O
F
CAN-ID
(11 Bit)
R
T
R
I
D
E
r
0
DLC
(4 Bit)
DATA
(0-8 Byte)
Checksum
(15 Bit)
D
E
L
A
C
K
D
E
L
EOF
(7 Bit)
Arbitration
Control
Data
Check
Acknowledge
Arbitration Bitrate
FD Data Bitrate (BRS = 1)
Arbitration Bitrate
S
O
F
CAN-ID
(11 Bit)
r
1
I
D
E
Arbitration
r
0
F
D
F
0 0 1 0
DLC
(4 Bit)
DATA
(0-64 Byte)
Checksum
(17/21 Bit)
StuffCNT (4 Bit)
D
E
L
EOF
(7 Bit)
A
C
K
D
E
L
Control
Data
Check
Acknowledge
B
R
S
E
S
I
Breaking reserved bits: new funtionality & incompatibility

---
Switching from CAN FD to CAN XL by using the reserved bit
S
O
F
CAN-ID
(11 Bit)
r
1
I
D
E
B
R
S
E
S
I
DLC
(4 Bit)
DATA
(0-64 Byte)
Checksum
(17/21 Bit)
StuffCNT (4 Bit)
D
E
L
A
C
K
D
E
L
EOF
(7 Bit)
Arbitration
Control
Data
Check
Acknowledge
0 0 1 1 0
X
L
F
S
O
F
PRIO
(11 Bit)
r
1
I
D
E
r
0
A
D
S
SDT
(8 Bit)
S
E
C
DLC
(11 Bit)
VCID
(8 Bit)
AF
(32 Bit)
DATA
(1-2048 Byte)
Check
sums
D
A
S
D
E
L
A
C
K
D
E
L
EOF
(7 Bit)
F
D
F
Arbitration
Control
Data
Check
Acknowledge
Arbitration Bitrate (CAN PHY)
XL Data Bitrate (DATA PHY)
Arbitration Bitrate
r
0
F
D
F
0 0 1 0
Breaking reserved bits: new funtionality & incompatibility

---
New/changed CAN XL frame content (simplified checksums)
0 0 1 1 0
X
L
F
S
O
F
PRIO
(11 Bit)
r
1
I
D
E
r
0
A
D
S
SDT
(8 Bit)
S
E
C
DLC
(11 Bit)
VCID
(8 Bit)
AF
(32 Bit)
DATA
(1-2048 Byte)
Check
sums
D
A
S
D
E
L
A
C
K
D
E
L
EOF
(7 Bit)
F
D
F
Arbitration
Control
Data
Check
Acknowledge
PRIO – 11 bit priority for arbitration (former 11 bit CAN Identifier)
ADS/DAS – switch sequence between arbitration and data phase
SDT – 8 bit Service Data Unit Type
SEC – 1 bit simple extended content (e.g. for security/segmentation)
DLC – 11 bit data length code (0 .. 2047) => 1 .. 2048 data bytes
VCID – 8 bit virtual CAN network identifier (analogue to VLAN identifier)
AF – 32 bit acceptance field (function depending on SDT)
DATA – 1 .. 2048 data bytes (depenting on DLC value)

---
Data structure layout for CAN FD in comparison to CAN XL
CAN FD data structure
CAN XL data structure (big endian representation of canfd_frame.can_id space)
struct canfd_frame {
        canid_t can_id; /* 32 bit CAN_ID + EFF/RTR/ERR flags */
        __u8 len; /* frame payload length in byte (0 .. 64) */
        __u8 flags; /* additional flags for CAN FD */
        __u8 __res0; /* reserved / padding */
        __u8 __res1; /* reserved / padding */
        __u8 data[64] __attribute__((aligned(8)));
};
struct canxl_frame {
        __u8 __res0; /* reserved / padding must be set to zero */
        __u8 vcid; /* virtual CAN network identifier */
        __u16 prio; /* 11 bit priority for arbitration */
        __u8 flags; /* additional flags for CAN XL */
        __u8 sdt; /* SDU (service data unit) type */
        __u16 len; /* frame payload length in byte (1 .. 2048) */
        __u32 af; /* acceptance field */
        __u8 data[2048];
};

---
Details of the data structure layout for CAN XL
struct canxl_frame {
        __u8 __res0; /* reserved / padding must be set to zero */
        __u8 vcid; /* virtual CAN network identifier */
        __u16 prio; /* 11 bit priority for arbitration */
        __u8 flags; /* additional flags for CAN XL */
        __u8 sdt; /* SDU (service data unit) type */
        __u16 len; /* frame payload length in byte (1 .. 2048) */
        __u32 af; /* acceptance field */
        __u8 data[2048];
};
vcid – contains values 0x00 .. 0xFF (0x00 = untagged / no VCID)
prio – shares the position and functionality with the 11 bit CAN ID in CAN CC/FD
flags – shares the position with the length (len) information in CAN CC/FD frames
To intentionally break with valid CAN CC/FD length values (0 .. 64) CANXL_XLF must be set in CAN XL frames:
#define CANXL_XLF 0x80 /* mandatory CAN XL frame flag (must always be set!) */
#define CANXL_SEC 0x01 /* Simple Extended Content (security/segmentation) */

---
CAN XL frame content: Service Data Unit Types (SDT)
Service Data Unit Types (0x00 .. 0xFF) – according to CAN CiA 611-1 (working draft)
0x00 : reserved
0x01 : Content based addressing
0x03 : CC CAN / CAN FD
0x04 : IEEE 802.3 (MAC frame)
0x05 : IEEE 802.3 (MAC frame) extended
0x06 : CAN CC
0x07 : CAN FD
0x08 : CiA 611-2 (Multi-PDU)
0x09 : AUTOSAR Multi-PDU
0x0A : CiA 613-2 (CANsec key agreement protocol)
0x0B .. 0xDF : reseved for future use
0xE0 .. 0xFE : manufacturer specific
0xFF : reserved

---
CAN XL summary
CAN XL is like „Ethernet with CSMA/CR arbitration“
High reliability (CRC/bitstuffing) with 10 Mbit/s data rate
CAN XL controller support CAN XL / CAN FD / CAN CC
CAN XL transceivers with switchable physical layer (arbitration/data)
Virtual CAN interface identifiers (analogue ethernet VLANs)
SDU (service data unit) types for multiple content use-cases